## Slide 1: CompTIA Network +
Chapter 3
Identifying Network components

## Slide 2: Objectives
What are the characteristics of various media types?
What is the role of a given network infrastructure component?
What features are provided by specified specialized network devices?
How are virtualization technologies impacting traditional corporate data center designs?
What are some of the primary protocols and hardware components found in a Voice over IP(VoIP) network?

## Slide 3: Identify Network Components
Many modern networks contain a daunting number of devices.
It is our job to understand the function of each device and how they work with each other.
The interconnection of these devices uses one of a variety of media (cables) types.

## Slide 4
The Media
By definition, a network is an interconnection of devices. Those interconnections occur over some type of media.
The media might be physical, such as a copper and fiber-optic cable or it might be the air, through which radio waves propagate.

## Slide 5
Coaxial Cable
Coaxial Cable is composed of two conductors.
  The inner, insulated conductor or center wire, passes the data.
  The outer, braided metal shield, which helps protect the data.

## Slide 6
Coaxial Cable
Three of the most common types of coaxial cables are;
  RG-6: Commonly used by local cable companies to connect individual homes.
  RG-58: This type of coaxial cable was popular with early 10BASE2 Ethernet networks.
  RG-59: Typical used to carry composite video between two nearby devices. (i.e. cable box to TV)
Although RG-58 was commonplace in early networks, coaxial cables role in modern computer networks is as the media used by cable modems

## Slide 7
Coaxial Cable
Common connectors used on coaxial cables:
BNC F-connector

## Slide 8
Twisted-Pair Cable
The most popular LAN media type is twisted-pair cable, where individually insulated copper strands are intertwined into pairs.
There are two categories of twisted pair:
  UTP – Unshielded Twisted Pair
  STP – Shielded Twisted Pair

## Slide 9: Unshielded Twisted-Pair Cable

## Slide 10: Shielded Twisted-Pair Cable

## Slide 11
Categories:
  CAT 3 (Category 3): up to 10 Mbps of data
  CAT 5 (Category 5): up to 100 Mbps throughput
  CAT 5e (Enhanced Category 5): higher twist ratio, up to 1000 Mbps throughput
  CAT 6 (Category 6): six times the throughput of CAT 5, used for 1000BASE-T
  CAT 6e (Enhanced Category 6): reduced attenuation and crosstalk, used for 10GBASE-T networks
CAT Ratings

## Slide 12: RJ-45

## Slide 13
Underwriters Laboratories and the National Electrical Code (NEC)
  Polyvinyl chloride (PVC) rating has no significant fire protection
    Lots of smoke and fumes
  Plenum-rated cable
    Less smoke and fumes
    Costs three to five times as much as PVC-rated cable
  Riser-rated cable for vertical runs
Cable Fire Ratings

## Slide 14
Fiber-Optic Cables
Contains glass or plastic fibers at core surrounded by layer of glass or plastic cladding
  Reflects light back to core

## Slide 15
Benefits over copper cabling:
  Nearly unlimited throughput
  Very high resistance to noise
  Excellent security
  Ability to carry signals for much longer distances before requiring repeaters than copper cable
  Industry standard for high-speed networking
Fiber-Optic Cables

## Slide 16
Multimode Fiber (MMF)
Uses a core with larger diameter than a single-mode fiber
  Common size 62.5 microns
Laser or LED generated light pluses travel at different angles.
Common uses
  Cables connecting router to a switch
  Cables connecting server on network backbone

## Slide 17
Multimode Fiber (MMF)
Transmission over multimode fiber-optic cable

## Slide 18
Single-Mode Fiber (SMF)
Uses a narrow core (< 10 microns in diameter)
  Laser generated light pluses travels over one path.
    Little reflection
  Light does not disperse
Accommodates
  Higher bandwidth, longer distances
  Connects carrier’s two facilities
Cost prohibit typical LANs, WANs use

## Slide 19
Transmission over single-mode fiber-optic cable
Single-Mode Fiber (SMF)

## Slide 20
MT-RJ (mechanical transfer-register jack) connector
LC (local connector)
ST (straight tip) connector
SC (subscriber connector or standard connector)
Common Connectors for Fiber

## Slide 21
Cable plant
  Hardware making up enterprise-wide cabling system
Standard
  TIA/EIA joint 568 Commercial Building Wiring Standard
Cabling Distribution

## Slide 22
Components
  Entrance facilities
  MDF (main distribution frame)
  Cross-connect facilities
  IDF (intermediate distribution frame)
  Backbone wiring
  Telecommunications closet
  Horizontal wiring
  Work area
Cabling Distribution

## Slide 23
TIA/EIA structured cabling in a building
Cabling Distribution

## Slide 24
Patch panel
Patch panel
Horizontal wiring
A standard TIA/EIA outlet
Cabling Distribution

## Slide 25
A typical UTP cabling installation
Cabling Distribution

## Slide 26
Cabling Distribution
66-block patch panel
110-block patch panel

## Slide 27
Wireless Technologies
Not all media is physical, as in the case of wireless network technologies.
All wireless devices connecting to the dame AP (Access Point) are considered to be on the same shared network segment.

## Slide 28
Network Infrastructure Devices
The devices used in a network infrastructure can vary on the layer 1 technology used.
  For example, a Token Ring network might use a multistation access unit (MSAU), while an Ethernet network might use a switch.
Because Ethernet-based networks are dominant today’s LANs, the infrastructure devices presented here lend themselves to networking using Ethernet as the Layer 1 transport.

## Slide 29
HUB
A HUB is at layer 1 of the OSI model.
  A HUB does not make forwarding decisions.
  A HUB receives bits in on one port and then retransmits those bits out all other ports.
  HUB most often use UTP cabling to connect to other network devices.
Three basic types of Ethernet HUBs exist.
  Passive HUB
  Active HUB
  Smart HUB (with SNMP)

## Slide 30: HUB
Regenerate and repeat signals
Used as network concentration points
Multiport repeater

## Slide 31: Bridges
A bridge joins together two or more LAN segments, typically two Ethernet LAN segments.
Each LAN segment is a separate collision domain.
A bridge makes intelligent forwarding decisions based on the destination MAC address present in a frame.
A bridge analyzes source MAC address information on frames entering the bridge and populates an internal MAC address table based on learned information.

## Slide 32: Bridges
Designed to create two or more LAN segments, each of which is a separate collision domain

## Slide 33: Switches
Like a bridge, switch can dynamically learn the MAC address attached to various ports by looking at the source MAC address on frames coming into a port.
Initially, however the switch is unaware of what MAC address reside off of which ports.
When a switch receives a frame destined for a MAC address not yet present in the switch’s MAC address table, the switch floods that frame out of all of the switch port, other than the port on which the frame arrived.

## Slide 34: Switches
Designed to create two or more LAN segments, each of which is a separate collision domain

## Slide 35: Multilayer Switches
Although a Layer 2 switch, makes forwarding decisions based on MAC address information, a multilayer switch can make forwarding decisions based on upper-layer information.
A multilayer switch could function as a router, and make forwarding decisions on IP address information.

## Slide 36: Multilayer Switches
Eight collision Domains, Two Broadcast Domain

## Slide 37: Routers
A Router is a layer 3 device, meaning that it makes forwarding decisions based on logical network address information. Such as IP addresses.
A router has the capability to consider high-layer traffic parameters in making its forwarding decisions.
Each port on a Router is a separate collision domain and a separate broadcast domain.
Routers are typically more feature-rich and support a broader range of interface types.

## Slide 38: Routers
Eight collision Domains, Two Broadcast Domain

## Slide 39: Infrastructure Devices Summary
Device | Number of Collision Domain Possible | Number of Broadcast Domains Possible | OSI Layer of Operation
HUB | 1 | 1 | 1
Bridge | 1 per port | 1 | 2
Switch | 1 per port | 1 | 2
Multilayer switch | 1 per port | 1 per port | 3+
Router | 1 per port | 1 per port | 3+

## Slide 40
PART II
Chapter 3
Identifying Network components

## Slide 41: VPN Concentrator
Companies with locations spread across multiple sites require secure communications between those sites.
One method is to create secure connections through an untrusted network, such as the Internet.
Such a secure tunnel is called a virtual private network (VPN).
The device that terminating these VPN tunnels, is a VPN Concentrator.
A VPN concentrator performs the processor-intensive process required to terminate multiple VPN tunnels.

## Slide 42: VPN Concentrator
VPN
Concentrator
VPN
Concentrator
VPN
Concentrator
VPN
Concentrator
Headquarters
Branch A
Branch B
Branch C

## Slide 43: Firewalls
A Firewall is primarily a network security appliance, is stands guard at the door of your network, protecting it from malicious Internet traffic.
There are many types of firewalls, a stateful firewall is one example.

## Slide 44: Firewalls
Stateful Firewall

## Slide 45: DNS Servers
A Domain Name System (DNS) server performs the task of taking a domain name like, www.ciscopress.com and resolving that name into a corresponding IP address.
Computers and the internet use numbers not names, but people recall names better than numbers.
www.ciscopress.com is an example of a fully-qualified domain name (FQDN)
An FQDN is a series of strings delimited by periods. The right-most string represents the root domain.

## Slide 46: DNS Servers

## Slide 47: DNS Hierarchy

## Slide 48: DHCP Servers
Most modern networks have IP address assigned to networking devices, and those logical Layer 3 addresses are used to route traffic between networks.
IP address can be statically configured on each host, however such process is time consuming and error prone (Manual).
A far more efficient method of IP address assignment is to dynamically assign IP addresses to network devices (Automatic).
This process assigns the; IP Address, Subnet Mask, Default Gateway, DNS Server to the host.

## Slide 49: DHCP Servers

## Slide 50: Proxy Servers
A Proxy Server is a device that makes request on behalf of its client.
Clients are configured to forward their packets, which are seemingly destined for the Internet, to a proxy server.
The proxy server evaluates the request, if it has a copy of the information the client is looking for it replies with it.
If the requested page is not in the server it forwards the request to the Internet.

## Slide 51: Proxy Servers

## Slide 52: Content Engines & Switches
Some networks do not use proxy servers, instead use a dedicated appliance to perform this content caching.
These appliances are commonly referred to as caching engines or content engines.
The Content Switches is also known as a load balancer, distributing incoming request across the various servers in the server farm.

## Slide 53: Content Engines

## Slide 54: Content Switch

## Slide 55: Virtual Network Devices

## Slide 56: VoIP Protocols & Components