## What You Need for This Project

- A Windows machine with Python on it, and the X-Lite softphone.  You created this machine in project 17: Fuzzing VOIP.

- The PBX server you made in project 16 using the 3CX phone system

- A Trixbox CD or ISO

The instructions below assume you are using two Vista computers in S214.

Setting Up

- Turn on the PBX server you set up on project 16: VoIP.  Just leave it running—this will be the Target Machine of the attacks from SIPVicious.

- Turn on the machine you installed Python on in Project 17: Fuzzing X-Lite with VoIPER.  This machine will be the Attacker Machine.

Downloading SIPVicious on the Attacker Machine

- SIPVicious is a +hacking suite for VoIP, containing these four tools.

- svmap - this is a sip scanner. Lists SIP devices found on an IP range

- svwar - identifies active extensions on a PBX

- svcrack - an online password cracker for SIP PBX

- svreport - manages sessions and exports reports to various formats

- On the Attacker Machine, open a Web browser and go to sipvicious.org

- On the right side of the page, click "Download SIPVicious".

- On the next page, click sipvicious-0.2.4.zip.

- Save the sipvicious-0.2.4.zip file on your desktop.

- On your desktop, double-click the sipvicious-0.2.4.zip file and click "Extract All…".  In the "Extract Compressed (Zipped) Folders" box, click Extract.

- A sipvicious-0.2.4 folder appears on your desktop.

- Double-click the sipvicious-0.2.4 folder to open it.  It contains a second folder, also named sipvicious-0.2.4.

Scanning for PBX Servers with svmap

- On the Attacker Machine, hold down the Shift key and right click the sipvicious-0.2.4 folder.  On the context menu, click "Open Command Window Here".

- In the Command Prompt window, type this command, and then press the Enter key:

svmap.py 192.168.1.1/24

That IP address range is correct for S214.  If you are working at home, your IP address range may be different.

- You should see your 3CXPhoneSystem PBX server detected, as shown above on this page .

Enumerating SIP Extensions with svwar

- On the Attacker Machine, in the Command Prompt window, type this command, and then press the Enter key:

svwar.py 192.168.1.10

Replace 192.168.1.10 with the IP address of your 3CXPhoneSystem PBX server, which you just found with svmap.

- The response is an error message, saying "server replied with an authentication request", as shown above on this page .  It suggests using the --force option.

- On the Attacker Machine, in the Command Prompt window, type this command, and then press the Enter key:

svwar.py 192.168.1.10 --force

Replace 192.168.1.10 with the IP address of your 3CXPhoneSystem PBX server.

- The response is still nothing but error messages—the PBX server is not vulnerable to this scanner.  It requires authentication, which makes sense.

Starting Trixbox-the VMware Asterix PBX Server

- You can run Trixbox on any computer that has VMware.  It can be the Target Computer, the Attacker Computer, or any other computer on the same LAN.

- You need the trixbox 2.0 VMware image.  I handed out CDs in class, but you can also download it from trixbox.org/trixbox-2-0-vmware-image-released

- Copy the whole CD to the hard disk.  The filenames say "Red Hat", but it is really running on CentOS Linux.

- Start VMware Player and open the Trixbox virtual machine.

- Log in as root with a password of trixbox (please note that the instructions on the download page give you the wrong password).

- You should see the message "Welcome to trixbox CE", as shown to the right on this page, along with a URL to use to manage trixbox.

- On the host Windows desktop, open a Web browser and go to the URL shown in the trixbox welcome message.

- At the main trixbox management page, click FOP.

- The FOP page opens, as shown to the right on this page, showing several extensions that are already programmed into trixbox.

Scanning for PBX Servers with svmap

- On the Attacker Machine, hold down the Shift key and right click the sipvicious-0.2.4 folder.  On the context menu, click "Open Command Window Here".

- In the Command Prompt window, type this command, and then press the Enter key:

svmap.py 192.168.1.1/24

That IP address range is correct for S214.  If you are working at home, your IP address range may be different.

- You should see both your 3CXPhoneSystem and Asterisk PBX servers detected, as shown above on this page.  When I did it, I had to restart the Target Computer to make the 3CXPhoneSystem visible.

## Capturing a Screen Image

- Make sure both your 3CXPhoneSystem and Asterisk PBX servers are visible. as shown above on this page .

- Press the PrintScrn key in the upper-right portion of the keyboard.

- On the host Windows system, Click Start, Programs, Accessories, Paint.  In the untitled - Paint window, select Edit, Paste from the menu bar.

- In the untitled - Paint window, click File, Save.  Select a Save as type of JPEG.  Save the document with the filename Your Name Proj 18a.

Enumerating SIP Extensions with svwar

- On the Attacker Machine, in the Command Prompt window, type this command, and then press the Enter key:

svwar.py 192.168.1.65

Replace 192.168.1.65 with the IP address of your Asterisk PBX server, which you just found with svmap.

- You should see several extensions located, from 200 through 204, as shown above on this page.

Cracking SIP Passwords with svcrack

- On the Attacker Machine, in the Command Prompt window, type this command, and then press the Enter key:

svcrack.py 192.168.1.65 –u 200

Replace 192.168.1.65 with the IP address of your Asterisk PBX server.

- The crack should work, finding the password for extension 200, which is 200, as shown above on this page.

- To see how the attack works, repeat it with higher verbosity.  On the Attacker Machine, in the Command Prompt window, type this command, and then press the Enter key:

svcrack.py 192.168.1.65 –u 200 -vv

Replace 192.168.1.65 with the IP address of your Asterisk PBX server.

- You can now see how the cracker works—it just tries three-digit number combinations in order until ir finds the password, as shown to the right on this page.  The cracker can also use a dictionary of passwords, but this simple attack is good enough for the demonstration accounts on your Asterisk PBX server.

## Connecting to the Asterisk PBS With Stolen Credentials

- On the Attacker Machine, if X-Lite is not running, double-click  the X-Lite icon on your desktop to start it.

- At the top left of the X-Lite window, click the ▼ symbol, and click "SIP Account Settings…", as shown to the right on this page.

- In the "SIP Accounts" box, click the Properties button.

- In the "Properties of Account1" box, change the User name and Password to 200

- In the "Properties of Account1" box, in the Domain field, change the IP address to the IP address of your Asterisk PBX server.

- In the "Properties of Account1" box, click OK.

- In the "SIP Accounts" box, click Close.

- The X-Lite panel should now show "Ready Your username is: 200", as shown to the right on this page.

## Capturing a Screen Image

- Make sure the "Ready Your username is: 200" message is visible, as shown to the right on this page .

- Press the PrintScrn key in the upper-right portion of the keyboard.

- On the host Windows system, Click Start, Programs, Accessories, Paint.  In the untitled - Paint window, select Edit, Paste from the menu bar.

- In the untitled - Paint window, click File, Save.  Select a Save as type of JPEG.  Save the document with the filename Your Name Proj 18b.

## Turning in Your Project

- Email the JPEG image to me as an attachment to an e-mail message.  Send it to:  cnit.124@gmail.com with a subject line of Proj 18 From Your Name, replacing Your Name with your own first and last name.  Send a Cc to yourself.

## Sources

http://forums.remote-exploit.org/showthread.php?t=12878'

http://sipvicious.org/webcasts/sipvicious-0.2-intro/web.html

Last Modified: 10-26-08