## Q1: How can you protect your eyes from glass shards?

## A1: Wear safety glasses

## Q2: How can you protect your eyes from infrared light damage?

## A2: Never look into a light source or a fiber that has power on it

## Q3: How can you make sure a fiver has no light in it?

## A3: Check it with a power meter

## Q4: How can you protect yourself from gas in manholes?

## A4: Test the air first, and then work with a harness and a partner outside the manhole.

## Q5: Fusion splicers are portable. Are there any places you cannot safely fusion splice?

## A5: You cannot safely fusion splice in a manhole because the fusing arc could ignite flammable gas.

## Q6: What is the most important safety concern in fiber optics?

## A6: Glass shards getting into skin or eyes

## Q7: What is a MSDS?

## A7: MSDS: Material Safety Data Sheet – a document that lists the risks of a chemical

## Q8: What hazards does canned compressed air present?

## A8: It can explode if heated or damaged, and some cans use a flammable propellant.

## Q9: What are the three ways to measure conduit cable lengths?

## A9: From prints (least accurate), with a measuring wheel (better), or measurement/pull tape (best).

## Q10: What percentage of additional cable length is typically needed, for inside and outside installations?

## A10: Typically 5% - 7% extra length is needed inside, and 1% extra length outside.

## Q11: What sort of splicing can be safely done in manholes?

## A11: Mechanical splicing can be done in manholes -- but not fusion splicing.

## Q12: What is innerduct?

## A12: Innerduct is flexible tubing inserted into large ducts to subdivide them.

## Last modified 6-15-06