## Q1: Why is cable plant documentation important?

## A1: To save time and material during installation, help in planning upgrades and troubleshooting, and because test data with loss measurements are usually required for acceptance by end user

## Q2: What data are required in cable plant documentation?

## A2: Cable manufacturer, type, length; Fiber type and size, splices and termination points, losses; Connections: types, locations, losses; Path of every cable; end connections; dark fibers (dark fibers are unused fibers available for future use)

## Q3: What skills are required for estimating installation costs?

## A3: Arithmetic, command of language and acronyms, imagination, handwriting, and computer skills.

## Q4: What are the three steps in estimating?

## A4: Takeoff, Writing up, Summarizing

## Q5: What is the working height for normal labor units?

## A5: Max. working height 12 feet

## Q6: What is the building height for normal labor units?

## A6: Building not exceeding three stories

## Q7: What are the labor units for Installing cable in conduit, 1-4 fibers?

## A7: 0.016 – 0.02 hours per foot

## Q8: What are the labor units for Installing cable in conduit, 144 fibers?

## A8: 0.05 – 0.065 hours per foot

## Q9: What are the labor units for Testing?

## A9: 0.12 – 0.24 hours per fiber

## Q10: What are the labor units for Terminating (polish required)?

## A10: 0.40 – 0.6 hours apiece

## Q11: Why do you need to include costs for removing old cable in estimates?

## A11: Because removal of old cable is required by the NEC, and it can be much more difficult than installing new cable

## Q12: What training costs are to be expected in estimates?

## A12: You may have to teach the owners or their representatives how to use the system, and handle phone calls from them later

## Q13: What is "overhead" in estimates?

## A13: Indirect costs, like site security, office space, insurance, etc. Overhead is higher in high-tech work, because it's more complex.