## Q1: When was the first fiber optic network installed?

## A1: In 1976, in Chicago. AT&T made it.

## Q2: What major communications networks are already running primarily on fiber?

## A2: Long-distance telephones, CATV, and the Internet backbone.

## Q3: What do FTTC and FTTH mean?

## A3: Fiber to the curb, and Fiber to the home

## Q4: What is SONET?

## A4: Synchronous Optical Network is a standard to enable telecommunications networks to interoperate

## Q5: What is SDH?

## A5: SDH (Synchronous Digital Hierarchy) is the international version of SONET

## Q6: What standard is threatening to replace SONET?

## A6: IP (Internet Protocol) and VoIP (Voice over Internet Protocol) may replace SONET.

## Q7: What is overbuilding, and when is it used?

## A7: CATV converts from copper to fiber by overbuilding -- attaching fiber to existing hanging cables, or pulling fiber through existing underground ducts

## Q8: What is the most common LAN standard?

## A8: Ethernet

## Q9: How fast is Ethernet, and what cables does it use?

## A9: Runs at 10 Mbps, 100 Mbps, 1 Gbps, or 10Gbps, can run over copper or fiber

## Q10: What are media converters, and why are they used?

## A10: Media Converters convert UTP Ethernet to Fiber Optics. This allows an Ethernet network to be greatly extended, mixing fiber and copper on the LAN.

## Q11: List four obsolete LAN standards that could use either copper or fiber

## A11: ARCnet, WangNet, DECnet, Token Ring

## Q12: List two obsolete LAN standards designed for fiber

## A12: Fiber Distributed Data Interface (FDDI) and Enterprise System Connection Architecture (ESCON)

## Q13: What is Fibre Channel used for?

## A13: Fibre Channel is used for server clusters and storage area networks

## Q14: What two networking standards are specialized for consumer electronics?

## A14: IEEE 1394 and TOSLINK are used for consumer electronics over copper or plastic optical fiber

## Q15: What two networking standards are specialized for automotive applications?

## A15: MOST (Media Oriented System Transport) connects media devices within the car, and Flexray connects safety devices like airbags

## Q16: What is fiber termination?

## A16: Termination is attaching connectors to the end of the fiber strands