## Q1: List the three layers outside the acrylate coating in a simplex fiber optic cable

## A1: Buffer, Kevlar strength member, and jacket, as shown

## Q2: When are loose-tube cables used?

## A2: Used for long distances and outside-plant

## Q3: How are loose-tube cables terminated?

## A3: With breakout kits, or fusion splicing to pre-connectorized pigtails

## Q4: How do loose-tube cables protect the fiber from water?

## A4: With gel or tape to block water, and armor to protect the cable from rodents

## Q5: When are breakout kits used?

## A5: To terminate fibers in loose-tube cables

## Q6: When are tight-buffer cables used?

## A6: Tight-buffer cables are the most common cables used indoors

## Q7: Can loose-buffer cables be used outdoors?

## A7: Yes, they are commonly used outdoors.

## Q8: Can tight-buffer cables be used outdoors?

## A8: No, because the buffer strains the fiber as temperature fluctuates, increasing attenuation

## Q9: What is a Distribution cable?

## A9: Several tight-buffer fibers bundled together with kevlar reinforcement and one jacket.

## Q10: When are distribution cables used?

## A10: Used for riser and office cabling

## Q11: How are distribution cables terminated?

## A11: They must be terminated inside a patch panel or junction box

## Q12: What is the outer diameter of the buffer in tight-buffer cable?

## A12: 900 microns

## Q13: What is a Breakout Cable?

## A13: Several tight-buffer fibers bundled together, each with its own with Kevlar reinforcement and jacket.

## Q14: Do Breakout Cables require Breakout Kits?

## A14: No. Each fiber can be broken out and individually connectorized.

## Q15: How do breakout cables compare with distribution cables?

## A15: Breakout cables are stronger, larger and more expensive than distribution cables

## Q16: When are breakout cables used?

## A16: They are used for Riser and Office Cabling

## Q17: What is a ribbon cable?

## A17: Dozens of fibers packed together, with buffer, strength member, and jacket outside.

## Q18: What type of cable is mass spliced or mass terminated?

## A18: Ribbon cable can be mass fusion spliced or mass terminated.

## Part 2

## Q1: What are the components of a duplex cable?

## A1: Two simplex cables, each containing tight-buffered fiber, strength member, and jacket, as shown.

## Q2: What is zipcord?

## A2: Zipcord is duplex cable

## Q3: What are simplex and zipcord cables used for?

## A3: Patch cables, short-run office cabling, test equipment.

## Q4: What are the components of a simplex cable?

## A4: Tight-buffered fiber, strength member, and jacket, as shown above.

## Q5: Can outside plant cable be used indoors?

## A5: No, because of fire safety only 50 feet of outsude cable can be used indoors.

## Q6: What is the difference between hybrid and composite cable?

## A6: Composite cable contains copper wires and fiber optics, and hybrid cable contains singlemode and multimode fibers

## Q7: What cable is rugged and used for patch cords?

## A7: Tight buffer, simplex or duplex

## Q8: What cable prevents rodent damage?

## A8: Armored cable

## Q9: What type of cable has many fibers, but can still be terminated with no breakout kit?

## A9: Breakout cable.

## Q10: What kind of cable has the highest fiber count in the smallest diameter?

## A10: Ribbon cable

## Q11: What bend radius is allowable while the cable is under tension?

## A11: 20 times the diameter

## Q12: What bend radius is allowable while the cable is not under tension?

## A12: 10 times the diameter

## Q13: What is a Figure-8 cable?

## A13: A cable with an attached wire for aerial installation

## Q14: What is an OGW cable?

## A14: Optical Ground Wire cables carry both electric power and fiber optic signals.

## Q15: What do the ratings OFN and OFC mean?

## A15: Optical Fiber Nonconductive, and Optical Fiber Conductive.

## Q16: What do the ratings OFNG and OFCG mean?

## A16: Optical Fiber Nonconductive General purpose, and Optical Fiber Conductive General purpose

## Q17: What do the ratings OFNR and OFCR mean?

## A17: Optical Fiber Nonconductive Riser-rated, and Optical Fiber Conductive Riser-rated. Riser cables can be used to go vertically between floors in a building.

## Q18: What do the ratings OFNP and OFCP mean?

## A18: Optical Fiber Nonconductive Plenum-rated, and Optical Fiber Conductive Plenum-rated. The Plenum is the area above the ceiling that carries ventilation.

## Q19: What does the rating OFN-LS mean?

## A19: Optical Fiber Nonconductive Low Smoke density

## Last modified 6-15-06