## Ch 6a: Losses and Connectors

## Q1: What is the difference between splices and connectors?

## A1: A permanent join is a splice. Connectors are used at patch panels, and can be disconnected.

## Q2: What are intrinsic loss factors at a join?

## A2: Problems the splicer cannot fix: Core diameter mismatch, Concentricity of fiber core or connector ferrules, Core ellipticity, Numerical Aperture mismatch

## Q3: What are extrinsic loss factors at a join?

## A3: Problems the person doing the splicing can avoid: Misalignment, Bad cleaves, Air gaps, Contamination, Reflectance

## Q4: What does a reflectance value of 20 dB mean?

## A4: A reflectance of 20 dB means that 1% of the light is reflected

## Q5: What are the acceptable loss and reflectance values for a singlemode splice?

## A5: Loss 0.15 dB, reflectance 50 dB.

## Q6: What are the acceptable loss and reflectance values for a singlemode connector pair?

## A6: Loss 1 dB, reflectance 30 dB.

## Q7: What are the acceptable loss and reflectance values for a multimode splice?

## A7: Loss 0.25 dB, reflectance 50 dB.

## Q8: What are the acceptable loss and reflectance values for a multimode connector pair?

## A8: Loss 0.75 dB, reflectance 25 dB.

## Q9: What type of connector is shown in the image?

## A9: ST, a 2.5 mm ferrule connector.

## Q10: What type of connector is shown in the image?

## A10: SC, a 2.5 mm ferrule connector.

## Q11: What type of connector is shown in the image?

## A11: FC, a 2.5 mm ferrule connector.

## Q12: What type of connector is shown in the image?

## A12: LC, a 1.25 mm ferrule connector.

## Q13: What type of connector is shown in the image?

## A13: MU, a 1.25 mm ferrule connector.

## Q14: What type of connector is shown in the image?

## A14: LX-5, a 1.25 mm ferrule connector.

## Q15: What type of connector is shown in the image?

## A15: FDDI, an old, bulky, duplex connector

## Q16: What type of connector is shown in the image?

## A16: ESCON, an old, bulky, duplex connector

## Q17: What type of connector is shown in the image?

## A17: MT-RJ, a newer Small Form Factor duplex connector.

## Q18: What type of connector is shown in the image?

## A18: Opti-Jack, a newer Small Form Factor duplex connector.

## Q19: What type of connector is shown in the image?

## A19: Volition, a newer Small Form Factor duplex connector.

## Q20: What type of connector is shown in the image?

## A20: Duplex LC, a newer Small Form Factor duplex connector.

## Ch 6b: Polish and Splices

## Q1: What are the three types of ferrule polish?

## A1: Flat PC, PC (domed), and APC (angled).

## Q2: What is FOCIS?

## A2: Fiber Optic Connector Intermateability Standard: A document produced by a connector manufacturer so others can mate to their connector

## Q3: What three types of adhesive are used for connectorization?

## A3: Epoxy (room temperature-cure or oven-cure), quick-curing anaerobic adhesives, and Hot-Melt.

## Q4: When are breakout kits used?

## A4: When connectorizing loose-tube cables or ribbon cables, because they contain bare fiber.

## Q5: What are the three mounting methods for connectors?

## A5: Adhesives, Crimping to hold the fiber, and Splicing to preconnectorized pigtails

## Q6: How does the epoxy-polish method compare to other connectorization methods?

## A6: Takes longer, but costs less and has lowest loss and reflectance

## Q7: How does the anaerobic adhesive method compare to other connectorization methods?

## A7: Faster than epoxy-polish but higher loss because polishing is difficult

## Q8: How does the crimping method compare to other connectorization methods?

## A8: Easier, but more expensive and more loss

## Q9: How does the pigtail splice method compare to other connectorization methods?

## A9: Very easy, but expensive and higher loss

## Q10: How does fusion splicing work?

## A10: Melts the fibers together to form a continuous fiber, using an expensive machine

## Q11: When is fusion splicing recommended?

## A11: Fusion splicing makes the strongest and best join for singlemode fiber, but it may lower bandwidth of multimode fiber.

## Q12: How does mechanical splicing work?

## A12: Mechanically aligns fibers, and contains index-matching gel to transmit light