## Q1: What are the two main types of hardware?

## A1: Premises Hardware – indoor, and Outside plant Hardware – outdoor

## Q2: How long can a backbone be in Premises cabling?

## A2: 2000 meters max.

## Q3: What is the Main Cross-Connect?

## A3: The start of a bulding's internal backbone; it should be near the data center or PBX

## Q4: What are Plug and Play assemblies?

## A4: Preterminated cable with SC or other connectors in a special sock for pulling, or MTP ribbon cable connectors (12 fibers in a single SC-size plug) that plugs into a preconnectorized patch panel

## Q5: What is an MTP connector?

## A5: A MTP ribbon cable connector connects 12 fibers in a single SC-size plug.

## Q6: What is the Intermediate Cross-Connect?

## A6: Connects interbuilding cable plant to intrabuilding cable plant

## Q7: What is the Telecom closet?

## A7: Transition from backbone to horizontal cable plant

## Q8: What is homerun cabling in a building?

## A8: Cables go from the Main Cross-Connect directly to the outlets, with only a single patch panel or splitter in between.

## Q9: What is a Splice Panel?

## A9: Hardware that holds and protects splices in one or more splice trays.

## Q10: What is a splice tray?

## A10: Hardware that holds and protects splices, usually 12 or 24.

## Q11: What is a Patch Panel?

## A11: Provides a centralized location for connecting fibers, testing, monitoring, and restoring riser or trunk cables

## Q12: What are splice closures?

## A12: Outside plant hardware to protect splices from water and the elements.

## Q13: What is conduit?

## A13: Pipes that protect cable

## Q14: What is innerduct?

## A14: Small pipes that sit inside conduit

## Q15: What is MCS Road Cable?

## A15: Cable designed to be inserted directly into a slit cut into pavement

## Last modified 6-15-06